## Slide 1
3-Bit Even Parity
Generator and Checker
Digital Logic Design Project
Abdul Rehman (2510115)

## Slide 2
Objective
Design, simulate, and analyze a 3-bit even parity generator and checker circuit using basic logic gates.
Demonstrate how parity bits enable simple error detection in digital data transmission.

## Slide 3
Introduction
A parity bit is an extra bit added to data so the total number of 1s is always even (even parity) or odd.
The Parity Generator creates this bit at the sender's end.
The Parity Checker verifies it at the receiver's end.
If parity doesn't match, a transmission error is detected.

## Slide 4
Parity Generator
P = A XOR B XOR C
Takes 3 data bits (A, B, C) and produces parity bit P using two cascaded XOR gates, so total number of 1s (A,B,C,P) is always even.
A | B | C | P
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 5
Parity Checker
E = A XOR B XOR C XOR P
Recomputes parity at the receiver using all 4 bits (A, B, C, P). If E = 0, data is correct; if E = 1, a transmission error is detected.
A | B | C | P | E
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0

## Slide 6
Tools Used
Logisim
Circuit simulation and logic verification against the truth table
TinkerCAD
Circuit design and visualization with virtual logic gate components
MS Word / PowerPoint
Project documentation and presentation

## Slide 7
Working Principle
1
3 data bits (A, B, C) enter the parity generator
2
Generator computes parity bit P using XOR gates
3
4-bit data (A, B, C, P) is transmitted to receiver
4
Checker recomputes parity across all 4 bits
5
E = 0 means data is correct; E = 1 flags an error

## Slide 8
Conclusion
This project demonstrates the design and simulation of a 3-bit even parity generator and checker using XOR logic gates. Truth tables verified through Logisim confirm correct parity generation and single-bit error detection — a foundational technique used in larger digital communication and memory systems.